## Slide 1
PRIORITY MAP
RIYADH HEATREADY
Urban growth and
surface heat screening
A priority map built from satellite data for southeast Riyadh
THE QUESTION
Where should a municipal planning team inspect first?
Team Milkaholics
Yusuf Karanib and Raed Mardoum
Notes: 0:00–0:20 | Yusuf. Good afternoon. We are Team Milkaholics. Our project is Riyadh HeatReady. It uses satellite data to rank one-kilometre cells in southeast Riyadh where urban growth, high surface temperature and modelled population overlap. We want to help answer one practical question: where should a municipal planning team inspect first?

## Slide 2
USER NEED AND SCOPE
A faster way to choose areas for inspection
02
168.30 km²
SOUTHEASTERN RIYADH STUDY AREA
1 km
TRANSPARENT SCREENING CELLS
1 user
MUNICIPAL PLANNING + HEAT TEAM
1 action
INSPECT LOCALLY BEFORE INTERVENTION
PROBLEM
Growth, heat, population and vegetation sit in separate layers. A planner still needs a short, explainable list of places to inspect.
OUTPUT
HeatReady combines the layers into a ranked list of 1 km cells for local review. Local checks come before any intervention.
Current limitation: we have not interviewed municipal users. A pilot must test whether this fits their workflow.
Notes: 0:55–1:50 | Yusuf. The study area covers 168.30 square kilometres on the southeastern edge of Riyadh. It is one part of the city, not all of Riyadh. Our intended user is a municipal planning and heat-resilience team. Growth, surface heat, population and vegetation can sit in separate layers, so staff still have to compare them before deciding where to inspect. HeatReady puts those layers into one ranked list of one-kilometre cells. It does not tell the user to plant trees or install a cool roof. It only suggests where to check first and compare with local plans and field conditions. We have not yet interviewed municipal users, so the first pilot must test whether this workflow is useful to them.

## Slide 3
TEAM
Our team
03
Yusuf Karanib
Project lead and demonstration
Leads the final submission. Explains how the satellite data becomes a priority map and runs the demonstration.
Raed Mardoum
Validation and pilot
Explains what the validation results mean and where the method is limited. Covers how planners could test the ranking in a municipal pilot.
Notes: 0:20–0:55 | Yusuf. I am Yusuf Karanib, the project lead. I will explain how the satellite data becomes a priority map and run the demonstration. Raed Mardoum will explain what the validation results mean, where the method is limited and how we would test the ranking with a municipal team.

## Slide 4
DATA AND METHOD
Data used in the analysis
04
Sentinel-2
Optical reflectance, vegetation and built features
Sentinel-1
Radar structure to reduce confusion in bright desert areas
Annual LULC
Six maps propose 2018–2023 built-up change
Landsat 8
2025 land surface temperature after quality masking
WorldPop
Modelled 2025 population exposure
Planet Tanager
426-band context and a test of a known desert error
Annual maps flag possible growth. Sentinel-1 and Sentinel-2 check whether it looks built-up. Heat, population and vegetation then produce the ranking.
Notes: 1:50–3:10 | Yusuf. We used six open data sources, and each one has a specific job. Sentinel-2 provides optical information about vegetation and built surfaces. Sentinel-1 adds radar structure, which helps because bright desert can look built-up in optical images. Six annual land-cover maps flag possible built-up change from 2018 to 2023. Landsat 8 provides land-surface temperature for 10 May 2025. WorldPop provides modelled population for 2025. Planet Tanager gives us a detailed spectrum for one date, which we use to test a known desert problem. We did not trust the annual change map by itself. It first flagged 13.82 square kilometres. We then kept only pixels where the 2025 optical and radar evidence also looked built-up. This left 3.74 square kilometres. We ranked the eligible one-kilometre cells using 40 percent heat, 30 percent population, 20 percent confirmed growth and 10 percent lack of vegetation. These weights are our PoC assumptions, not municipal policy.

## Slide 5
WORKING OUTPUT
Priority map and GIS files
05
3.74 km²
CONFIRMED GROWTH SIGNAL
14 / 67
HIGH / ELIGIBLE CELLS
78.7
TOP SCORE: R05C10
The HTML report shows the map and a table of the top five zones. Separate CSV, GeoJSON and GeoTIFF files support further review.
Notes: 3:10–4:45 | Yusuf. [On slide 5] The result is a decision map and a component chart. Sixty-seven cells contain confirmed growth, and fourteen are labelled High priority. R05C10 ranks first with a score of about 78.7. Its score does not come from one hidden prediction; the chart shows the heat, population, growth and vegetation components. [Open outputs/dashboard.html and stay at Decision output.] This dashboard is a self-contained static report, not an interactive application. Here are the headline metrics, the decision map and the top-five table. The stricter rule retained 3.74 square kilometres of confirmed growth, and the top row is R05C10. The repository also contains separate CSV, GeoJSON and GeoTIFF files so a planner can review the same result in a spreadsheet or GIS. [Return to slide 5.] This output is a screening result. It cannot choose an intervention by itself; every high-ranked zone still needs local inspection. Raed will now explain what our validation proves, what the method adds, and how we would test it with a municipality.

## Slide 6
VALIDATION
Validation results and main limitations
06
0.88
F1 AGREEMENT
0.78
INTERSECTION OVER UNION
0.89
BALANCED ACCURACY
These numbers show agreement with a separate WorldCover reference. Field checks are still needed.
MAIN LIMITATIONS
Land surface temperature cannot measure air temperature or personal heat exposure.
WorldPop estimates population from a model. It does not provide a live census or worker count.
Bright desert and roofs can still confuse classification.
Score weights are PoC assumptions that a real user must review.
Notes: 4:45–5:55 | Raed. To test the built-up model, we trained in the western part of the study area, tuned in a separate middle strip and tested in the east against ESA WorldCover. The east-side holdout reached an F1 score of 0.88, an intersection over union of 0.78 and balanced accuracy of 0.89. F1 balances missed built-up pixels and false alarms. Intersection over union measures overlap. Balanced accuracy gives equal weight to built and unbuilt classes. These numbers show agreement with another satellite product; they are not field accuracy. Landsat measures land-surface temperature, not air temperature or personal heat exposure. WorldPop is modelled and may miss worker exposure. Bright desert and roofs can still confuse classification. The score weights are assumptions that a real user must review. Because of these limits, HeatReady supports inspection rather than making an automatic decision.

## Slide 7
APPROACH
Evidence from several satellite sources
07
METHOD
Annual land cover maps flag possible growth.
Optical and radar images check whether the area still looks built-up.
The output shows every part of the score and includes the GIS evidence.
One Tanager scene adds spectral context for a single date. It cannot prove change or identify materials.
POSSIBLE BENEFIT
A planner can review one ranked list instead of comparing several separate layers. This still needs user testing.
Notes: 5:55–6:55 | Raed. HeatReady does not depend on one index. The annual maps flag possible change, and separate optical and radar evidence check whether the area still looks built-up. We also tested a common shortcut: using a high NDBI value as proof of built land. In the Tanager scene, likely-unbuilt desert had a higher median narrow-band NDBI than established built land, so one threshold can fail here. The Tanager image gives extra spectral context for one date. It cannot prove change or identify a material. Each ranked cell keeps its score parts and GIS evidence. This could make screening faster, but we need real users to test that before we claim a benefit.

## Slide 8
NEXT STEP
Proposed municipal pilot
08
1
Interview
Confirm the decision, current workflow and acceptable false alarms with at least three real users.
2
Field check
Inspect the top five zones, record useful results and false alarms, and compare with local plans.
3
Adjust
Agree on weights, add worker exposure and city-plan constraints, then rerun the ranking.
4
Repeat
Test the same process in another Riyadh area before making an operational claim.
PILOT REQUEST
Test HeatReady with one municipal team and measure useful findings, false alarms and time spent.
Notes: 6:55–7:55 | Raed. Our next step is a small municipal pilot. First, we would speak with at least three planners, GIS staff or heat-resilience stakeholders and confirm how they currently choose areas to inspect. Second, they would review the top five cells against local plans and field observations, and record useful findings and false alarms. Third, we would adjust the weights and add missing local information such as worker exposure and city-plan constraints. Finally, we would repeat the test in another Riyadh area and measure the time, cost and repeatability. We are asking for support to run that pilot and find out whether HeatReady actually helps a municipal team. Thank you. We are ready for your questions.

## Slide 9
APPENDIX
Data sources and dates
09
Source | Dates used | Role | Access / licence
Sentinel-2 L2A | 11 May 2018; 10 May 2021; 9 May 2025 | Optical features, masks, vegetation | Copernicus open access
Sentinel-1 RTC | 10 May 2018; 6 May 2021; 9 May 2025 | Radar structure | Microsoft PC; CC BY 4.0
IO/Esri annual LULC | 2018–2023 | Trend + candidate endpoint change | CC BY 4.0
Landsat 8 C2 L2 | 10 May 2025 | Land-surface temperature | US public domain
ESA WorldCover | 2021 | Spatial holdout reference | CC BY 4.0
WorldPop Global2 | 2025 | Modelled population | CC BY 4.0
Planet Tanager | 15 May 2025 | Spectral context + sensitivity test | Open urban archive; CC BY 4.0
Item IDs, processing steps and licences are documented in the repository. Satellite 813 imagery was not used.
Notes: Appendix only. Open if a judge asks for exact source dates, roles or licences.

## Slide 10
Validation evidence and limits
Training area: west Tuning area: middle Test area: east
RESULTS
The east-side holdout was compared with WorldCover.
F1 0.88, IoU 0.78 and balanced accuracy 0.89.
The test contains 36,156 reference pixels.
LIMITS
Field accuracy.
Air temperature or health outcomes.
Municipal approval or user acceptance.
Next: field and user review of the top-ranked cells.
APPENDIX
10
Notes: Appendix only. Use for questions about leakage, train-test geography, annual trend uncertainty or the difference between satellite agreement and field accuracy.