## Slide 1
PRIORITY MAP
RIYADH HEATREADY
Where should planners
inspect first?
Satellite and population data for southeast Riyadh
WHAT IT GIVES
A ranked map of 1 km areas that may need an early site visit
Team Milkaholics
Yusuf Karanib and Raed Mardoum
Notes: 0:00-0:15 | Yusuf. Good afternoon. We are Team Milkaholics, and this is Riyadh HeatReady. We used satellite and population data to answer a simple question: when a planning team has limited time, which parts of southeast Riyadh should they inspect first?

## Slide 2
PROBLEM AND SOLUTION
The problem we focused on
02
168.3 km²
AREA WE STUDIED
1 km
SIZE OF EACH CELL
Planners
WHO THIS IS FOR
Inspect first
WHAT THE TOOL SHOWS
PROBLEM
Planners may need to compare separate maps for growth, heat, population and vegetation before choosing where to visit.
OUR IDEA
HeatReady combines those maps and ranks 1 km areas. It gives planners a place to start, not a final decision.
We still need to test this with real municipal users.
Notes: 0:15-0:55 | Yusuf. In our study area, the information a planner needs is spread across separate maps. One map shows growth, another heat, another population and another vegetation. Comparing them takes time. HeatReady combines them and ranks one-kilometre areas. The highest-ranked areas are the places we suggest checking first. It does not choose an intervention or make a planning decision. A local team would still compare the result with city plans and visit the area. We have not interviewed municipal users yet, so that is an important next step.

## Slide 3
TEAM
Who we are
03
Yusuf Karanib
Project lead and demo
Explains the data, method and result. Runs the live demonstration.
Raed Mardoum
Validation and city test
Explains the accuracy numbers, the limits and how a city team could test the idea.
Notes: 0:55-1:10 | Yusuf. I am Yusuf, and I will explain the data, method and demo. Raed will cover the validation, the limits and how we would test HeatReady with a municipal team.

## Slide 4
DATA AND METHOD
How we built the ranking
04
Sentinel-2
Shows vegetation and surface colour
Sentinel-1
Radar check for built structures
Annual land cover
Flags possible growth from 2018 to 2023
Landsat 8
Measures land surface temperature
WorldPop
Estimates where people live
Planet Tanager
Tests a desert classification problem
Annual maps find possible growth. Optical and radar data check it. Heat, population and vegetation complete the score.
Notes: 1:10-2:15 | Yusuf. We used open satellite data, and each source had one job. Annual land-cover maps showed where built-up land may have appeared between 2018 and 2023. We checked those areas with Sentinel-2 optical images and Sentinel-1 radar, because bright desert can sometimes look like buildings. Landsat gave us land surface temperature, WorldPop gave a population estimate, and Sentinel-2 also gave vegetation. The annual maps first flagged 13.82 square kilometres. After the optical and radar checks, 3.74 square kilometres remained. We then scored each eligible one-kilometre area: 40 percent heat, 30 percent population, 20 percent confirmed growth and 10 percent low vegetation. These weights are starting assumptions for this proof of concept. A real user should review them.

## Slide 5
RESULT AND DEMO
What HeatReady produced
05
3.74 km²
CONFIRMED GROWTH SIGNAL
14 / 67
HIGH / ELIGIBLE CELLS
78.7
TOP SCORE: R05C10
The same result is available as a map, a table and GIS files.
Notes: 2:15-3:45 | Yusuf. Here is the result. Sixty-seven cells contained confirmed growth, and fourteen were labelled high priority. R05C10 ranked first with a score of about 78.7. The chart shows why: its score combines heat, population, growth and vegetation. It is not a hidden prediction. [Open outputs/dashboard.html and go to Decision output.] The report shows the same map and a short table. Here is R05C10 at the top. A planner can also use the result as a CSV, GeoJSON or GeoTIFF file in a spreadsheet or GIS. [Return to slide 5.] A high score means inspect this area early. It does not mean a specific project should start there. Raed will now explain the validation, the limits and what makes this method different.

## Slide 6
VALIDATION
What the validation tells us
06
0.88
F1 AGREEMENT
0.78
INTERSECTION OVER UNION
0.89
BALANCED ACCURACY
The model matched a separate satellite reference well. This is not the same as field accuracy.
MAIN LIMITATIONS
Surface temperature is not air temperature or personal heat exposure.
WorldPop is an estimate, not a current population or worker count.
Bright desert and roofs can still confuse the model.
A real user still needs to review the score weights.
Notes: 3:45-4:40 | Raed. We tested the built-up model on the eastern part of the study area, separate from the training area, using ESA WorldCover as a reference. It reached an F1 score of 0.88, an overlap score of 0.78 and balanced accuracy of 0.89. In simple terms, the model and the satellite reference agreed well. But this does not prove field accuracy. Landsat measures surface temperature, not air temperature or personal heat exposure. WorldPop is an estimate, not a live population count. Bright desert and roofs can still confuse the model. The weights in our final score are also our choices. HeatReady should guide inspection, not make an automatic decision.

## Slide 7
DIFFERENCE
What is different about our approach
07
THREE CHECKS
Annual maps suggest where growth may have happened.
Optical and radar data check the same places.
Each final score keeps its four parts visible.
The Tanager test showed why one built-up index can be misleading in bright desert.
WHY IT HELPS
A planner gets one ranked list and can still see the evidence behind each area.
Notes: 4:40-5:20 | Raed. The main difference is that we do not rely on one image or one index. Annual maps suggest where growth may have happened, then optical and radar data check that signal. In the Tanager scene, unbuilt desert scored higher than established built land on a common built-up index. This shows why one threshold can mislead us. Each final score also keeps its four parts visible, so a planner can see why an area ranked highly.

## Slide 8
NEXT STEP
How we would test it next
08
1
Talk to users
Ask planners and GIS staff how they choose inspection areas today.
2
Check the top five
Compare the ranking with local plans and visits to the area.
3
Fix the score
Adjust the weights and add local information that we are missing.
4
Test again
Run the same process in another part of Riyadh.
THE TEST
Does HeatReady save time without sending staff to the wrong places?
Notes: 5:20-6:15 | Raed. Our next step is small and practical. First, we would meet planners or GIS staff and learn how they choose areas today. Then we would check the top five HeatReady areas against local plans and field observations. We would record which results were useful and which were false alarms. Based on that, we would change the weights and add missing local information, such as worker exposure or planned projects. Finally, we would repeat the test in another part of Riyadh. The goal is to learn whether HeatReady saves time without sending staff to the wrong places. Thank you. We are ready for your questions.

## Slide 9
APPENDIX
Data sources and dates
09
Source | Dates used | Role | Access / licence
Sentinel-2 L2A | 11 May 2018; 10 May 2021; 9 May 2025 | Optical features, masks, vegetation | Copernicus open access
Sentinel-1 RTC | 10 May 2018; 6 May 2021; 9 May 2025 | Radar structure | Microsoft PC; CC BY 4.0
IO/Esri annual LULC | 2018-2023 | Trend + candidate endpoint change | CC BY 4.0
Landsat 8 C2 L2 | 10 May 2025 | Land-surface temperature | US public domain
ESA WorldCover | 2021 | Spatial holdout reference | CC BY 4.0
WorldPop Global2 | 2025 | Modelled population | CC BY 4.0
Planet Tanager | 15 May 2025 | Spectral context + sensitivity test | Open urban archive; CC BY 4.0
Item IDs, processing steps and licences are documented in the repository. Satellite 813 imagery was not used.
Notes: Appendix only. Open if a judge asks for exact source dates, roles or licences.

## Slide 10
Validation evidence and limits
Training area: west Tuning area: middle Test area: east
RESULTS
The east-side holdout was compared with WorldCover.
F1 0.88, IoU 0.78 and balanced accuracy 0.89.
The test contains 36,156 reference pixels.
LIMITS
Field accuracy.
Air temperature or health outcomes.
Municipal approval or user acceptance.
Next: field and user review of the top-ranked cells.
APPENDIX
10
Notes: Appendix only. Use for questions about leakage, train-test geography, annual trend uncertainty or the difference between satellite agreement and field accuracy.